## Slide 1: Beyond Conventional Nitrate Isotopes Multi-isotope Fingerprinting Of Nutrient Contamination In South Florida Surface Waters
MGWA 2026
Arash Sharifi , Sean Ahearn, Zeneida Cernada, Kevin Reagan, Marlon Garcia, Keiran Swart and Stephany Rubin Mason
Isobarscience.com
info@isobarscience.com
Betalabservices.com
info@betalabservices.com
Notes: Intro Slide
Top: Add Presentation Title, Bottom: Add Presenter Name(s) (Name, Affiliation)

## Slide 2
Outline
Background
Background
Crash course on Isotope systematics and notation
What is Isotope?
Isotope systematics and notation
Isotope in Environment
Florida’s Aquifer System
Climate and Human Impact
Sources of Contamination
Materials and Methods
Sampling Sites
Analytics
Results
Source Assessment
Water Characterization
Conclusion
Image Credit: Visible Earth, NASA
DISCLAIMER: This presentation is the property of SGS Isobar Science and may not be distribute, reproduced, or modified without the prior written consent from SGS Isobar Science.
Copyright ©2025. SGS Isobar Science. All Rights Reserved

## Slide 3
Background
Isotopes: isos (“equal”) + topos (“place)
Atoms with the same number of protons but different numbers of neutrons
What is Isotope?
Lighter isotopes (those with less neutrons) are generally more abundant in the environment.
Some isotopes are radioactive and unstable. they called Radioisotopes and they decay into more stable form
Some isotopes never been observed to decay radioactively and are referred to as Stable Isotopes

## Slide 4
Backgrou(nd
Isotope systematics and notation
Abundance of different isotopes in the environment conventionally presented as a ratio relative to each other
87Sr/86Sr
Sometimes this ratios are compared to known international standards and presented with  notation
Ratio (R) = 18O/16O
18O=[(Rsample/Rstandard)-1]1000

## Slide 5
Background
Isotope in Environment
Rayleigh Distillation
Based on the atomic weights, some isotopes are behaving differently in the environment.
18O=0
18Ov=-12
18Ov=-15
18Ov=-17
18Ov=-21
18Or=-3
18Or=-5
18Or=-11

## Slide 6
Background
Isotope in Environment
Isotopic ratios can have specific range for different materials

## Slide 7
Background
Bataille et al. 2012, Chem. Geology
Geology
Groundwater
Isotope in Environment

## Slide 8
Florida’s Aquifer System
Background
Surficial Aquifer System
Floridan Aquifer System (Confined or unconfined)
Spans an area of 260,000 km2
Underling four states; FL, AL, GA, SC
Supply water to 11 million Floridians
DISCLAIMER: This presentation is the property of SGS Isobar Science and may not be distribute, reproduced, or modified without the prior written consent from SGS Isobar Science.
Copyright ©2025. SGS Isobar Science. All Rights Reserved

## Slide 9
Under the climate change scenario, demand for agricultural irrigation will increase leading to water shortage across Florida and create conflicts over availability of freshwater
Devitt et al., 2012
Background
Climate Impact
DISCLAIMER: This presentation is the property of SGS Isobar Science and may not be distribute, reproduced, or modified without the prior written consent from SGS Isobar Science.
Copyright ©2025. SGS Isobar Science. All Rights Reserved

## Slide 10
Human Impact
Natural flow of water is disturbed to accommodate water supply for heavily populated areas and vast agricultural fields
Background
DISCLAIMER: This presentation is the property of SGS Isobar Science and may not be distribute, reproduced, or modified without the prior written consent from SGS Isobar Science.
Copyright ©2025. SGS Isobar Science. All Rights Reserved

## Slide 11
Cui et al., 2016, Environ Earth Sci
Susceptible to contamination from land use practices
Vulnerable to nitrogen contamination
Shallow water table depth, high nitrate concentrations
Human Impact
Background
DISCLAIMER: This presentation is the property of SGS Isobar Science and may not be distribute, reproduced, or modified without the prior written consent from SGS Isobar Science.
Copyright ©2025. SGS Isobar Science. All Rights Reserved

## Slide 12
Sources of Contamination
Nonpoint sources and point sources contamination can be difficult to distinguish.
When mitigating nutrients or developing wetland project it is necessary to understand the sources of nutrients into and out of a system.
Background
DISCLAIMER: This presentation is the property of SGS Isobar Science and may not be distribute, reproduced, or modified without the prior written consent from SGS Isobar Science.
Copyright ©2025. SGS Isobar Science. All Rights Reserved

## Slide 13
Six sites were randomly selected in S Florida
Water samples were analyzed for
δ18O
δ2H
δ18ONO3
δ15NNO3
δ18OPO4
δ 11B
87Sr/86Sr
Materials and Methods
DISCLAIMER: This presentation is the property of SGS Isobar Science and may not be distribute, reproduced, or modified without the prior written consent from SGS Isobar Science.
Copyright ©2025. SGS Isobar Science. All Rights Reserved

## Slide 14
Effect of hot and humid climate of the region on shaping the local meteoritic water line
Putman et al., 2019, WRR
Results
DISCLAIMER: This presentation is the property of SGS Isobar Science and may not be distribute, reproduced, or modified without the prior written consent from SGS Isobar Science.
Copyright ©2025. SGS Isobar Science. All Rights Reserved

## Slide 15
Oxygen and nitrogen isotopes of nitrate can be used to trace the source of nitrate in water,
Source regions are greatly overlapped and is hard to pinpoint a contamination source
Results
DISCLAIMER: This presentation is the property of SGS Isobar Science and may not be distribute, reproduced, or modified without the prior written consent from SGS Isobar Science.
Copyright ©2025. SGS Isobar Science. All Rights Reserved

## Slide 16
Boron isotope, tracer for source of contamination
Chart: δ11B (‰)
| -15.76521 | -0.75072426999999997
Natural Ca-borate | 0.1 | 0.1
Natural Na-borate | 0.15 | 0.15
Synthetic Ca-borate | 0.2 | 0.2
Synthetic Ca-borate | 0.2 | 0.2
Synthetic Na-borate | 0.2 | 0.2
Synthetic Na-borate | 0.2 | 0.2
Synthetic Na-borate | 0.2 | 0.2
Freshwater (Inland Aquifer) | 0.25 | 0.25
Freshwater (Coastal Aquifer) | 0.25 | 0.25
Domestic Wastewater | 0.35 | 0.35
Seawater | 0.3
Sewage-contaminated Groundwater | 0.4 | 0.4
Results
DISCLAIMER: This presentation is the property of SGS Isobar Science and may not be distribute, reproduced, or modified without the prior written consent from SGS Isobar Science.
Copyright ©2025. SGS Isobar Science. All Rights Reserved

## Slide 17
Combining δ15NNO3 with δ11B provides a better distinction between the sources of nutrients
Results
DISCLAIMER: This presentation is the property of SGS Isobar Science and may not be distribute, reproduced, or modified without the prior written consent from SGS Isobar Science.
Copyright ©2025. SGS Isobar Science. All Rights Reserved

## Slide 18
Wide range of δ18OPO4
Correlation with Sr isotope
Sr isotopic signature of pollutants must be established
Chart: δ18OPO4 (‰)
| 2.6325000000000003 | 0 | 19.271000000000001 | 12.779 | 2.5190000000000001 | 23.843
87Sr/86Sr | 0.70912 | 0.70904 | 0.70847 | 0.70871 | 0.70902 | 0.70915
Results
DISCLAIMER: This presentation is the property of SGS Isobar Science and may not be distribute, reproduced, or modified without the prior written consent from SGS Isobar Science.
Copyright ©2025. SGS Isobar Science. All Rights Reserved
Chart: 1/Srng/g 1000
| 6.1996354376136118 | 2.4831118637517018 | 5.8921388235385423 | 4.2895818892885256 | 2.9525553862644074 | 6.5519320703683359
87Sr/86Sr | 0.70912 | 0.70904 | 0.70847 | 0.70871 | 0.70902 | 0.70915
Chart: δ18OPO4 (‰)
| 15.498799999999999 | 25.377099999999999
Chemical Fertilizer | 0.61111 | 0.61111
Fertilizer Ore | 1.0222 | 1.0222
WWT Effluent USA | 1.4222 | 1.4222
WWT Effluent Europe | 1.4222 | 1.4222
Detergent | 1.8111 | 1.8111
Toothpaste | 2.2222
Animal Faeces | 2.6111 | 2.6111
Soil Leachate | 3 | 3
Compost | 3.4 | 3.4
Vegetable Leachate | 3.8 | 3.8
 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 19
Results
Water samples can be characterized based on multiple isotopic values
DISCLAIMER: This presentation is the property of SGS Isobar Science and may not be distribute, reproduced, or modified without the prior written consent from SGS Isobar Science.
Copyright ©2025. SGS Isobar Science. All Rights Reserved

## Slide 20
Pinpointing the source of contamination by adding boron isotope to the traditional O and N isotope
Oxygen isotope of dissolved phosphate and Sr isotopic ratio provide more information on type of the pollutants
Characterization of water based on multiple isotopic values
Conclusion