## Slide 1
The Influence of Groundwater Modeling
on the Concept of groundwater Age
Parc Darcy
Dijon, France

## Slide 2
“Beneath the ground surface in stratified formations,
sometimes there are actual underground watercourses that flow with appreciable velocities in fissures, crevices, or natural cavities,
and sometimes there are aquifers derived from infiltration through sand that flow slowly between two impermeable beds.
I will not cite all the examples …. invoked in support of the existence of this double fact, which cannot be contested.”
Darcy 1856

## Slide 3
Unconfined (A) and Confined (B) Aquifers
Plate 22 Darcy 1856
Note that Darcy’s confined aquifers are the thin units, with high permeability

## Slide 4
Dupuit 1867
Loss of hydraulic head in Paris Basin
Darcy and Dupuit observed a parabolic change in hydraulic head moving along the aquifer
If flow were laminar the loss of head downgradient would have been linear.
Ground water flow is therefore occurring in conduits and porous media, not just porous media

## Slide 5
“There are two general methods by which water finds its way through the strata:
in the one—the rocks being close-textured—the water passes through fissures formed by fracture, or tubular channels formed by solution;
in the other—the rock being open-textured—the water seeps through the pores, permeating the whole bed.”
Chamberlin 1885
Notes: Image for Tony – A negative test in this case is that this well is not “artesian”. Well is cased down to layer A. Higher artesian head from layer B is lost to layer A.

## Slide 6
Dual/Triple Permeability
Höfer von Heimhalt noted not only that there is both matrix and fracture porosity in bedrock (plus cave porosity in carbonates and gypsum) but also that there will be exchange of water between them.
Höfer von Heimhalt
1912

## Slide 7
Three principal types of underground openings:
Pores – the characteristic openings of pervious granular materials, which are intricately interconnected and chiefly of capillary size [Pore Water]
Open fractures – occur chiefly in dense crystalline or cemented rocks, the master fractures fed by tributaries of capillary size [Fracture Water]
Large tubular or cavernous openings – solutional openings in limestone and flowage tunnels in lavas [Karst Water]
(Tolman 1937)
The key point is these are not separate and independent…
Groundwater is flowing in all three systems simultaneously.

## Slide 8
Active flow at all scales
Triple Porosity Aquifers
Matrix / Fractures & Bedding Planes / Conduits

## Slide 9
What happened?
Early and longstanding recognition of the importance
of multiple permeability pathways was lost.
Toth 1963
Notes: Freeze and Cherry 1979 Textbook “Groundwater”. Was it a printing error a statement that the authors were overturning conventional logic.

## Slide 10
Since, for such flow, the velocity diminishes rapidly with distance from the well, then it is clear that only exceptionally will rates of flow in ground water be encountered that are outside the upper range of validity of Darcy's law.
M. King Huppert
1940

## Slide 11
M. King Huppert 1940
Isotropic Homogeneous Flow

## Slide 12
Toth
1963
Three types of flow system: Local, intermediate, regional
The flow system shown here is 38 miles wide and 2 miles deep. Of course it is all perfectly isotropic and homogeneous???
Notes: The flow system shown here is 38 miles wide and 2 miles deep. Of course it is perfectly isotropic and homogeneous???

## Slide 13: Aquifers
Idealized
Multiple Porosities
Anisotropic
Inhomogeneous
Mathematically Challenging
Single Porosity
Isotropic
Homogeneous
Mathematically Tractable
Real

## Slide 14
Provides a consistent method to interpret tracer data
- But is only a starting point for age interpretation
Piston Flow

## Slide 15
Advection and Dispersion
Tracer Adsorption/Retardation

## Slide 16
2-D flow with 6 heterogeneity domains
At a given time there is a range of travel distance

## Slide 17: Challenges
Lithostratigraphic nomenclature presumes homogeneous sediments.
Aquifers are heterogeneous at the human scale. Aquifers are not isotropic and homogeneous at any useful scale.
Porous media models based on isotropic, homogeneous assumptions and currently dominate hydrogeologic theory, practice and regulation. – Porous media is the default assumption.
Hydrogeologists need a fast, economical way to evaluate the assumption of porous media.

## Slide 18
Real World Observations
Groundwater doesn’t care how fancy your computer model is
Mathematical Solutions
Computer Models
Identify Controlling Factors
Groundwater will flow thru all available pathways finding the optimal solution
Construct Better Models and Reiterate

## Slide 19: Computers are just a tool
Don’t let a computer program limit how you answer a question
E. Calvin Alexander, Jr.